Launch a python program on startup

Source: http://www.instructables.com/id/Raspberry-Pi-Launch-Python-script-on-startup/

1. Make a launcher script
“camera_reader_launcher.sh” for our program

----------------------------------------
#!/bin/sh
# launcher.sh

cd /
cd home/pi/Github/RPi_Camera_Reader
sudo python mainVideoCapture.py
cd /
-----------------------------------------

2. Make it executable
$ chmod 755 camera_reader_launcher.sh

Test it with following command:
$ sh camera_reader_launcher.sh

3. Add auto-launch at startup using Crontab
create a log folder in home directory
$ cd
$ mkdir logs

add to crontab:
$ sudo crontab -e

enter the line at the end of the file:
@reboot sh /home/pi/..../camera_reader_launcher.sh >/home/pi/logs/cronlog 2>&1

4. Reboot
The program should now start automatically at reboot:
$ reboot

Important Note:
the function “raw_input” only works for Python 2 which is the default version in raspberry pi. If the version changes to Python 3, this function should be replaced by “input()”.

Camera V2

The specs can be found in the following website:
https://www.element14.com/community/docs/DOC-81672/l/new-pi-camera-and-pi-camera-noir-v2

In a nutshell, the camera resolution and frame rate are 1080p at 30fps, 720p at 60 fps, and 640 by 480p at 90 fps.

Important Note:
There is a trade-off between high-resolution and file of view as described in:
https://picamera.readthedocs.io/en/release-1.10/fov.html

Specifically, a 1080p resolution (HD) limits the field of view.

To convert the default h264 video format to MP4, AVI, or others, follow the steps below:

- Download “gpac”
$ sudo apt-get install gpac

- Call command to convert
MP4Box -add original_video converted_video